## Slide 1: YAMM Yet Another Memory Manager
Andrei Vintila, Ionut Tolea
Amiq Consulting

## Slide 2: Agenda
Theory
  Memory Management Introduction
  YAMM Overview: Features, Algorithm, Datatypes, API
Comparison with UVM_MAM
  Feature-wise
  Performance-wise
Examples

## Slide 3: Memory Management – What is it?

## Slide 4: Memory Management Requirements
Real Life | Verification
Provide memory buffers to programs | Support real life use cases
Prevent memory corruption | Provide randomization support
Reduce fragmentation | Provide debug support
 | Not necessarily a memory model

## Slide 5: YAMM Features (1)
Implementations for SystemVerilog, C++
Everything is a buffer
Provides API for retrieval of allocated buffers
Supports multiple allocation modes
Supports memory granularity and address alignment
Provides buffer content management

## Slide 6: YAMM Features (2)
Buffers represent address spaces themselves
Memory can be written to file or pretty-printed
Provides usage and fragmentation statistics
Can be easily extended for specific use cases

## Slide 7: YAMM Data Types
yamm_buffer
  Contains all data and functions
yamm
  Top level instance of the memory manager
  Inherits yamm_buffer
yamm_access
  Optional usage
  Used to model a basic access (start address, size)

## Slide 8: YAMM Overview - Algorithm
After initialization the memory map will contain a single FREE buffer
All buffers in a memory map are chained in a double linked list

## Slide 9: YAMM Overview – API (1)
Allocation
  Manual allocation: insertion
  Automatic allocation rules:
    RANDOM_FIT
    FIRST_FIT (and FIRST_FIT_RND)
    BEST_FIT (and BEST_FIT_RND)
    UNIFORM_FIT
Deallocation
  It can be done on a specific buffer or address

## Slide 10: YAMM Overview – API (2)

## Slide 11: YAMM Overview – API (3)
Search functions
  Retrieve buffers by name
  Retrieve buffers by address
  Retrieve buffers in address range
  Retrieve buffers by access
Debug functions
  Return the memory map allocation as a string
  Dump memory map to file
  Provide usage and fragmentation statistics

## Slide 12: YAMM – Use case
A typical use case would be a DUT that handles accesses to a memory with specific priorities.
When using constraint random overlapping accesses can be generated which increases the difficulty of checking.

## Slide 13: YAMM – Use case (2)
YAMM can be easily used to generate interesting scenarios, by providing the buffers in which the accesses are done (address and size)

## Slide 14: YAMM – Use case (3)
Checking is made much easier when YAMM is used to control the buffers in which the writes/reads are done.

## Slide 15: MAM – UVM Solution
Oriented towards memory modeling
MAM is used with UVM_MEM to reserve specific memory regions
Supports only “greedy” allocation mode
Specific regions can be freed or entire memory can be wiped
Memory state can be returned as a string

## Slide 16: MAM vs YAMM – Feature Wise (1)
Memory
  UVM_MAM is linked to UVM_MEM which provides the memory locations used for storing data
  YAMM top level as well as every individual buffer contains a memory map composed of multiple buffers that can store simple data
Allocation
  UVM_MAM can only allocate on previously unallocated memory (2 allocation modes)
  YAMM can allocate new buffers in either unallocated memory or inside an already allocated buffer (6 allocation modes)

## Slide 17: MAM vs YAMM – Feature Wise (2)
Finding buffers
  UVM_MAM provides only an iterator; user must implement the search functions
  YAMM provides support for finding and modifying buffers by different criteria

## Slide 18: MAM vs YAMM – Feature Wise (3)
Ease of use
  UVM_MAM is complex and rather hard to use and for features beyond reserving and freeing regions user has to go to objects higher in hierarchy
  YAMM has a more user friendly API, memory map can be accessed by calling functions on the top level and also specific regions can be accessed by calling same functions on the chosen buffers

## Slide 19: Performance test - Parameters
Memory space of 1G
Allocation of 5000 buffers of size 100
Measuring the time taken for allocation every 100 allocations
For MAM, request_region() with default policy
For YAMM, allocate_by_size() with RANDOM_FIT allocation mode was used

## Slide 20: Performance test – MAM vs YAMM
More than 200x the speed

## Slide 21: Examples – Initialization Example
yamm new_memory;
yamm_size_width memory_size = 10000;
new_memory = new;
new_memory.build(“memory_name”, memory_size);

## Slide 22: Examples – Sequence Example
class user_sequence extends uvm_sequence;
rand int unsigned access_size;
...
task body();
yamm_buffer buffer = p_sequencer.user_memory.allocate_by_size(access_size);
`uvm_do_with(user_item, {
address == buffer.get_start_addr();
size == buffer.get_size();
data == buffer.get_contents();
})
endtask
endclass

## Slide 23: Examples – Scoreboard example
class user_scoreboard;
yamm user_memory;
...
//function checks if the current access is done to a previously allocated address
function void check_access(user_item item);
if(user_memory.get_buffer(item.addr) == null)
`uvm_error(get_name(), "Access detected to a non-allocated memory address!")
endfunction
endclass

## Slide 24: YAMM Availability
Open Source under Apache 2.0 license
Available in both SystemVerilog and C++ as well
Blog: www.amiq.com/consulting/blog
Github: www.github.com/amiq-consulting/yamm

## Slide 25: Questions